## Slide 1: Vibration Analysis of Tapered Truncated cantilever beams using Deep Learning
Naman Yadav
Asim Tewari
Department of Mechanical Engineering, IIT Bombay
IMEC 2019

## Slide 2: Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values
  Graphical comparison with actual values
Extrapolation Analysis
  Prediction ability over unseen data range
Conclusion
Future Research

## Slide 3: Overview
Motivation

## Slide 4: motivation
Some problems are really difficult or impossible to solve theoretically.
In some cases these can be solved by fitting curve to some data-points generated for special cases.
Data driven approach:
  Removes necessity of field specific knowledge.
  There is a large amount of data present.
    Highly optimized algorithms are there to process this data.
  Tremendous computational power available.

## Slide 5
Overview
Motivation
Deep Learning Model

## Slide 6: Deep Learning Model
Training data was generated using MATLAB.
Neural network features:
  Activation function: PReLU
  Loss function: Mean squared percent error
  Optimizer: Adam optimizer
Training of Neural network was done on Python using PyTorch.

## Slide 7: Input Variables
Variation in cross-sectional properties:
(where, )
are inputs to the neural network.

## Slide 8: Neural network Architecture
Input Layer
(2 units)
Hidden Layer
(without activation)
(6*N2 units)
Hidden Layers
(with activation and normalisation)
(L1 layers and N1 units in each layer)
Output Layer
(6 units)
Hidden Layer
(without activation)
(6*N2 units)

## Slide 9: Output variables
Output variables
β1, β2, β3, δ21, δ31, δ32 (6 variables)
  β1, β2, β3 are the natural frequency parameters
  δ21, δ31, δ32 are the node locations

## Slide 10: Actual Variation of Output Variables
Euler-Bernoulli equation
Using variable separation
General solution of
  where, , ,
    Jη and Yη are ηth order Bessel Functions of first and second kind, respectively.
    Iη and Kη are modified ηth order Bessel Function of first and second kind, respectively.
Boundary conditions

## Slide 11: Actual Variation of Output Variables
After applying boundary conditions we will get 4 linear equations:
After solving Δ = 0, we can get values of β = βr, where, r is the mode number. From which, we can compute and using following relations,
,
Finally, mode shapes can be obtained as follows,

## Slide 12: Actual Variation of Output Variables

## Slide 13
Overview
Motivation
Deep Learning Model
Data Generation

## Slide 14: Data Generation
η є [0, 3], δ0 є [2e-3, 0.56] => 301*15,000 datapoints.
η є [3, 10], δ0 є [7e-2, 0.56] => 701*15,000 datapoints.
For η є [0, 10], data from the two cases was merged:
  η є [0, 3], δ0 є [2e-3, 0.56] => 301*15,000 = 4,515,000.
  η є (3, 10], δ0 є [7e-2, 0.56] => 700*15,000 = 10,500,000.
In total 15,015,000 datapoints were generated.
But only a fraction was used for training.

## Slide 15
Overview
Motivation
Deep Learning Model
Data Generation
Model Training

## Slide 16: Model Training
Training and validation data
  Generated data was shuffled.
  Few data points were sampled from shuffled data to train the neural network.
  Some datapoints for validation were also selected.
Test data
  A separate data set was created by randomly sampling points.
Results
  Trained model was evaluated over the unseen test dataset to report the results.

## Slide 17
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results

## Slide 18: Training Parameters
Table 1: Deep Learning model training parameters |  | 
 | SD (Small Dataset) | BD (Big Dataset)
# Training datapoints | 2*211 | 20*211
# Validation datapoints | 1,000 | 
# Iterations | 30,000 | 
Initial Learning Rate | 0.01 | 
Update period | 5,000 | 
Update factor | 5 | 

## Slide 19: Training Results
 | SD (Small Dataset) | BD (Big Dataset)
# Training datapoints | 2*211 | 20*211
L1 | 3 | 7
N1 | 173 | 207
N2 | 3 | 3
SN (Small Network)
BN (Big Network)

## Slide 20: Training Results

## Slide 21
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values

## Slide 22: Percent Deviations
Table 2: For η є [0, 3], δ0 є [2e-3, 0.56] |  |  |  | 
Output | Mean Percent dev. |  | Max. Percent dev. | 
 | SD-SN | BD-BN | SD-SN | BD-BN
β1 | 0.022 | 0.011 | 0.115 | 0.106
β2 | 0.020 | 0.008 | 0.110 | 0.071
β3 | 0.021 | 0.009 | 0.111 | 0.052
δ21 | 0.016 | 0.012 | 0.172 | 0.101
δ31 | 0.024 | 0.013 | 0.317 | 0.255
δ32 | 0.012 | 0.007 | 0.159 | 0.083
Table 3: For η є [3, 10], δ0 є [7e-2, 0.56] |  |  |  | 
Output | Mean Percent dev. |  | Max. Percent dev. | 
 | SD-SN | BD-BN | SD-SN | BD-BN
β1 | 0.019 | 0.011 | 0.130 | 0.079
β2 | 0.018 | 0.010 | 0.130 | 0.046
β3 | 0.019 | 0.010 | 0.123 | 0.054
δ21 | 0.013 | 0.009 | 0.090 | 0.050
δ31 | 0.019 | 0.009 | 0.169 | 0.051
δ32 | 0.010 | 0.005 | 0.055 | 0.037

## Slide 23
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values
  Graphical comparison with actual values

## Slide 24: Comparison Between Actual And Predicted Values

## Slide 25: Comparison Between Actual And Predicted Values

## Slide 26
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values
  Graphical comparison with actual values
Extrapolation Analysis

## Slide 27: Extrapolation Analysis
Data was then split back into two parts as generated:
  Part 1: η є [0, 3], δ0 є [2e-3, 0.56]
  Part 2: η є [3, 10], δ0 є [7e-2, 0.56]
Models corresponding to SD and BD mentioned earlier were trained on one part and then evaluated on the other to see its extrapolation capabilities.

## Slide 28
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values
  Graphical comparison with actual values
Extrapolation Analysis
  Prediction ability over unseen data range

## Slide 29: Trained On Part 1 Evaluated over Part 2
Table 4: Trained over η є [0, 3] and evaluated over η є [3, 10] |  |  |  | 
Output | Mean Percent dev. |  | Max. Percent dev. | 
 | SD-SN | BD-BN | SD-SN | BD-BN
β1 | 12.922 | 19.327 | 26.671 | 40.068
β2 | 7.082 | 12.582 | 19.416 | 31.156
β3 | 3.737 | 8.609 | 13.828 | 23.150
δ21 | 1.866 | 8.318 | 7.643 | 21.166
δ31 | 2.919 | 7.453 | 7.816 | 20.621
δ32 | 1.331 | 4.310 | 3.593 | 11.100

## Slide 30: Percent Deviation Variation
SD-SN
N1 – 3
L1 – 173
N2 - 3
BD-BN
N1 – 7
L1 – 207
N2 - 3

## Slide 31: Trained On Part 2 Evaluated over Part 1
Table 5: Trained over η є [3, 10] and evaluated over η є [0, 3] |  |  |  | 
Output | Mean Percent dev. |  | Max. Percent dev. | 
 | SD-SN | BD-BN | SD-SN | BD-BN
β1 | 10.620 | 4.630 | 94.813 | 57.242
β2 | 6.181 | 1.808 | 58.538 | 19.544
β3 | 4.826 | 1.361 | 45.678 | 10.128
δ21 | 7.060 | 3.664 | 121.945 | 80.435
δ31 | 9.475 | 4.975 | 202.181 | 134.401
δ32 | 3.174 | 1.408 | 43.375 | 27.963

## Slide 32: Percent Deviation Variation
SD-Sn
N1 – 3
L1 – 173
N2 - 3
BD-BN
N1 – 7
L1 – 207
N2 - 3

## Slide 33
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values
  Graphical comparison with actual values
Extrapolation Analysis
  Prediction ability over unseen data range
Conclusion

## Slide 34: Conclusion
 | Small Neural Network | Large Neural Network
Simple trend in Training Data compared to evaluation data | Not Recommended | Recommended
Complex trend in Training Data compared to evaluation data | Recommended | Not Recommended

## Slide 35
Overview
Motivation
Deep Learning Model
Data Generation
Model Training
  Training parameters and results
  Percent deviations of predicted values
  Graphical comparison with actual values
Extrapolation Analysis
  Prediction ability over unseen data range
Conclusion
Future Research

## Slide 36: Future Research
These models can also be trained on data for beams subjected to other boundary conditions.
  Due to similar underlying equations, we can expect reasonably high accuracy in predictions.
Other better models could be developed to improve the extrapolation accuracy of the neural network far away from trained range.
  Challenging part in doing this is the complex nature of Bessel functions, which contain integrations of factorial, factorials in denominator, etc.

## Slide 37: Thank You
Questions ?